## Slide 1: Efficient Sequential Consistency in GPUs via Relativistic Cache Coherence
Xiaowei Ren and Mieszko Lis
The University of British Columbia

## Slide 2
Contributions :
GPU Sequential Consistency GPU Best Relaxed Consistency
Performance Gap: from 28% to 7%
Two Possible Solutions :
Change Core Microarchitecture
Improve Cache Coherence Protocol

## Slide 3: Cost of SC : store stalls
sync through
Invalidation
messages
- longer latency
Idealized MESI (no latency for inv-ack): 1.6x faster
A valid in $
ld A
C0
C1
dir
time
st A
execution continues
inv
ack

## Slide 4: Cost of SC in Temporal Coherence
A valid in $ until t=100
ld A
st A
sync through
shared clock
C0
C1
100
time
dir
+ can support SC
— wait until lease expires
Shim et al. Library Cache Coherence. MIT CSAIL TR 2011-027, 2011.
Singh et al. Cache Coherence for GPU Architectures. In HPCA 2013.
TC: 88% faster than MESI
execution continues
TC-SC: 28% slower than TC
+ no write stalls
— cannot support SC
ld A(hit)
Problem

## Slide 5: Removing SC Stalls : RCC
ld A
new A valid until C1’s now=21
now=11
now=0
now=11
now=15
ld B
B valid until C0’s now=25
sync through
distributed
logical clocks
st A
now=11
now=0
C0
C1
dir
now=0
now=0
physical time
ld A
now=0
now=0
A valid until C0’s now=10
+ no write stalls
Store: advance clock of writing core to the logical time store should happen
Load: advance clock of reading core to the logical time data were written
A is invalidated after
clock advancement
ld A(hit)
Assume B was written @ 15
Earliest timestamp later than 10

## Slide 6: Distributed Logical-clocks in CPUs ?
 | CPU* | GPU
need speculation ? | Yes | No
downgrade ? | Yes | No
invalidation message ? | Yes | No
recall message ? | Yes | No
implementation ? | Complex | Simple
CPU : private $ write-back
shared $ write-back
GPU : private $ write-through
shared $ write-back
CPU : latency-critical
GPU : throughput-oriented, latency-tolerant
Lamport. Time, Clocks, and the Ordering of Events in a Distributed System. Comm. ACM, 21:558–565, 1978.
*Yu & Devadas. TARDIS: Timestamp-based Coherence Algorithm for Distributed Shared Memory. In PACT 2015.

## Slide 7: Simple Implementation
core
state
exp
exp
exp
exp
ver
ver
ver
ver
ver
ver
exp
exp
exp
exp
exp
exp
now
tag
tag
tag
tag
tag
tag
data
data
data
data
data
data
v
d
v
d
v
d
v
d
v
d
v
d
L2$ state
tag
v
tag
v
tag
v
tag
v
L1$
state
data
data
data
data
now, ver and exp are 32-bit.
Area Overhead :
3% for L1 $
6% for L2 $

## Slide 8: Simple Implementation
 | MESI | TC-SC | TC | RCC
L1 states | 16 | 5 | 5 | 5
L1 transitions | 81 | 27 | 42 | 33
L2 states | 15 | 8 | 8 | 4
L2 transitions | 50 | 23 | 34 | 14

## Slide 9: Stall cost improved?
Stalls caused by SC
52% less than MESI
25% less than TC-SC
0.0
0.2
0.4
0.6
0.8
1.0
MESI
TC-SC
RCC

## Slide 10: Overall Performance
0.0
0.25
0.5
0.75
1.0
1.25
MESI
TC-SC
RCC
intra-workgroup sharing (right):
10% faster than MESI
3% faster than TC-SC
inter-workgroup sharing (left):
76% faster than MESI
29% faster than TC-SC
0.0
0.5
1.0
1.5
2.0
MESI
TC-SC
RCC

## Slide 11: So, cost of full SC support in GPUs?
0.0
0.25
0.5
0.75
1.0
1.25
RCC
TC
0.0
0.25
0.5
0.75
1.0
1.25
RCC
TC
Inter-Workgroup Sharing (left):
7% slower than TC
Intra-Workgroup Sharing (right):
3% slower than TC

## Slide 12: Summary
Resolve SC stalls with distributed logical clocks.
RCC is 29% better than TC-SC, which is the best SC model so far.
RCC shortens the performance gap between SC and the best RC within 7%.
Questions?
Main source of SC inefficiency : stalls for write permission acquisition.